## Slide 1
SIGNALS & SYSTEMS | PROJECT UPDATE
ECG-Based Sleep Apnea
Detection Using a CNN
Progress achieved through the current Jupyter notebook
SIGNAL PROCESSING
WINDOWING
1D CNN
EVALUATION
Current scope: ECG pipeline implemented; SpO₂ pipeline remains future work.
SYSTEMS & SIGNALS • PROJECT PROGRESS
01

## Slide 2
01 / PROJECT FRAMING
Project objective & current scope
What we are building
A prototype that classifies ECG windows as Normal or Apnea using a one-dimensional convolutional neural network.
Why it matters
Sleep-apnea events can affect oxygen levels and cardiovascular activity. ECG provides a non-invasive signal for exploring automated screening.
Completed
ECG loading, annotations, preprocessing, windows, patient-level split, CNN training and test evaluation.
In progress
Refinement of threshold selection, evaluation and reproducibility.
Not yet done
SpO₂ branch, ECG + SpO₂ fusion, real-time streaming.
SYSTEMS & SIGNALS • PROJECT PROGRESS
02

## Slide 3
02 / END-TO-END WORKFLOW
Pipeline implemented in the notebook
01
Load ECG
WFDB records + apnea annotations
→
02
Preprocess
0.5–40 Hz Butterworth band-pass filter
→
03
Segment
60 s windows = 6,000 samples at 100 Hz
04
Label + split
Normal/Apnea labels; patient-level split
→
05
Train CNN
1D convolutions + pooling + dense output
→
06
Evaluate
Accuracy, ROC-AUC, confusion matrix, class metrics
SYSTEMS & SIGNALS • PROJECT PROGRESS
03

## Slide 4
03 / DATA
Dataset preparation & segmentation
Source
PhysioNet Apnea-ECG database; ECG recordings and minute-based apnea annotations.
Signal format
Sampling rate: 100 Hz. Each 60-second window contains 6,000 samples.
Preprocessing
Fourth-order Butterworth band-pass filter from 0.5 to 40 Hz; windows normalized.
7,038
windows assembled
14
patients used
4,391
Apnea windows
2,647
Normal windows
Data note: recording a02 was skipped because WFDB could not load its samples correctly. The remaining 14 recordings were used in this notebook run.
SYSTEMS & SIGNALS • PROJECT PROGRESS
04

## Slide 5
04 / SIGNALS & SYSTEMS
Signal-processing work completed
• Loaded raw ECG and inspected sampling frequency, duration and annotations.
• Removed baseline drift using a moving-average estimate during exploratory analysis.
• Applied low-pass smoothing in the initial exploration, then implemented a Butterworth band-pass filter for the main dataset pipeline.
• Detected R-peaks and derived RR intervals and instantaneous heart rate for exploratory analysis.
• Mapped apnea annotations to minute-level windows and checked label consistency.
From waveform to usable windows
Raw ECG
↓
Filtered ECG
↓
60 s window
↓
Normalized input
Exploratory RR/heart-rate analysis is separate from the final raw-window CNN input.
SYSTEMS & SIGNALS • PROJECT PROGRESS
05

## Slide 6
05 / EXPERIMENTAL DESIGN
Patient-level split to reduce leakage
Training
4,061
Validation
1,528
Testing
1,449
Patient groups
Train: a04, a05, a06, a07, a09, a10, a12, a15
Validation: a03, a08, a14
Test: a01, a11, a13
The notebook verifies that no patient appears in more than one split.
SYSTEMS & SIGNALS • PROJECT PROGRESS
06

## Slide 7
06 / MODEL
CNN baseline architecture
Input
6,000 × 1
→
Conv1D + BN + Pool
32 filters, kernel 7
→
Conv1D + BN + Pool
64 filters, kernel 5
→
Conv1D
64 filters, kernel 3
→
Global average pooling
Temporal summary
→
Dense + Dropout
32 units; dropout 0.2
→
Sigmoid output
Apnea probability
Training configuration
• Adam optimizer (learning rate 0.0003)
• Binary cross-entropy; accuracy and AUC tracked
• Early stopping on validation loss
Model size
25,409 total parameters
25,217 trainable parameters
Training stopped after 11 epochs in the recorded run.
SYSTEMS & SIGNALS • PROJECT PROGRESS
07

## Slide 8
07 / EVALUATION
Preliminary test-set results
76.26%
Accuracy
0.8649
ROC–AUC
84%
Apnea precision
78%
Apnea recall
Confusion matrix at threshold = 0.40
 | Pred Normal | Pred Apnea
Actual Normal | 375 | 139
Actual Apnea | 205 | 730
What this means
• The model identifies 730 of 935 apnea windows at the chosen threshold.
• 205 apnea windows are missed; false negatives remain a key concern.
• The 0.40 threshold improves apnea recall compared with the default 0.50 threshold.
These are notebook-run results, not a reproduction of the paper's reported metrics.
SYSTEMS & SIGNALS • PROJECT PROGRESS
08

## Slide 9
09 / SUMMARY
Current status: a working ECG baseline
What has been achieved
• End-to-end ECG pipeline from PhysioNet records to labeled windows.
• Signal filtering, normalization and patient-independent data splits.
• Trained 1D CNN with saved model and evaluation artifacts.
• Preliminary test accuracy of 76.26% and ROC–AUC of 0.8649.
Prototype for an academic course project. Not a clinical diagnostic tool.
SYSTEMS & SIGNALS • PROJECT PROGRESS
10