## Slide 1
ECG Signal Processing for Sleep Apnea Analysis

## Slide 2
1. What the Code Does
End-to-end signal-processing workflow
Loads an ECG record from the Apnea-ECG dataset using WFDB.
Extracts the first ECG channel and inspects its sampling frequency and samples.
Visualizes the first 10 seconds of the raw ECG signal.
Reads apnea annotations associated with the record.
Preprocesses the ECG by centering, baseline removal, and low-pass filtering.
Detects R-peaks, then calculates RR intervals and instantaneous heart rate.
ECG Signal Processing • 2

## Slide 3
2. Libraries & Data
Main packages and record used in the notebook
NumPy — numerical arrays and signal operations.
Pandas — imported for data handling.
Matplotlib — ECG and heart-rate visualization.
scikit-learn — train/test split, scaling, and classification metrics are imported, but no ML model is trained in this notebook.
WFDB — reads PhysioNet-style ECG records and annotations.
SciPy — used later for R-peak detection with find_peaks.
Record loaded: a01 from the Apnea-ECG raw-data directory.
ECG Signal Processing • 3

## Slide 4
3. Loading the ECG Signal
WFDB reads the physiological waveform
record = wfdb.rdrecord("../data/data/raw/apnea-ecg/a01") ecg = record.p_signal[:, 0] fs = record.fs print("Signal shape:", record.p_signal.shape) print("Sampling frequency:", fs) print("Channels:", record.sig_name)
Key variables
record → full WFDB record
ecg → first ECG channel
fs → sampling frequency
annotation → apnea labels
ECG Signal Processing • 4

## Slide 5
4. Signal Inspection & Annotations
Understand the raw ECG before preprocessing
The notebook plots the first 10 seconds of ECG against time.
Apnea annotations are loaded with wfdb.rdann(..., 'apn').
The code prints annotation sample positions, corresponding times, and symbols.
These annotations provide event information associated with the ECG record.
annotation = wfdb.rdann( "../data/data/raw/apnea-ecg/a01", "apn" ) print(annotation.sample[:20]) print(annotation.symbol[:20]) # ECG visualization plt.plot(np.arange(samples) / fs, ecg[:samples])
ECG Signal Processing • 5

## Slide 6
5. Preprocessing: Centering & Baseline Removal
Reduce slow signal drift before peak detection
Raw ECG
ecg
Centering
subtract mean
Baseline
moving average
Detrended
ecg_detrended
First, the DC offset is removed: ecg_centered = ecg − mean(ecg).
A moving-average window of 0.8 seconds estimates the baseline.
The estimated baseline is subtracted from the centered ECG.
The notebook compares the original centered signal with the baseline-removed signal.
ECG Signal Processing • 6

## Slide 7
6. Low-Pass Filtering
Smooth the detrended ECG before detecting R-peaks
lp_window_seconds = 0.08 lp_window = int(lp_window_seconds * fs) ecg_filtered = np.convolve( ecg_detrended, np.ones(lp_window) / lp_window, mode="same" )
Purpose
Smooth high-frequency fluctuations
Retain the main ECG waveform shape
Create a cleaner signal for peak detection
Compare detrended vs filtered ECG
ECG Signal Processing • 7

## Slide 8
7. R-Peak Detection
Identify heartbeat locations using threshold + minimum distance
from scipy.signal import find_peaks min_distance = int(0.5 * fs) threshold = np.mean(signal) + 0.5 * np.std(signal) peaks, properties = find_peaks( signal, height=threshold, distance=min_distance )
signal is the filtered ECG.
Minimum peak distance = 0.5 seconds, limiting detections to roughly 120 beats/min or less.
Threshold = mean(signal) + 0.5 × standard deviation.
find_peaks returns the detected peak sample indices.
ECG Signal Processing • 8

## Slide 9
8. RR Intervals & Heart Rate
Convert R-peak timing into cardiac features
# Time between consecutive R-peaks rr_intervals = np.diff(peaks) / fs # Instantaneous heart rate heart_rate = 60 / rr_intervals # Time associated with each RR interval rr_time = peaks[1:] / fs plt.plot(rr_time, heart_rate)
RR interval
Δt = (peakᵢ₊₁ − peakᵢ) / fs
Heart rate
HR = 60 / RR
Output
Heart rate in BPM
ECG Signal Processing • 9

## Slide 10
9. Complete Processing Pipeline
What happens from the file to the final feature
ECG record
WFDB
Extract channel
p_signal[:,0]
Center
remove mean
Detrend
0.8 s baseline
Filter
0.08 s moving avg
R-peaks
find_peaks
RR intervals
peak differences
Heart rate
60 / RR
Final result of the notebook: a time series of instantaneous heart rate derived from detected ECG R-peaks.
The heart-rate series can serve as an input feature for later sleep-apnea analysis.
ECG Signal Processing • 10

## Slide 11
10. Current Scope & Next Step
Important distinction between preprocessing and classification
Implemented in this notebook:
  ECG loading and visualization
  Apnea annotation reading
  Signal centering, baseline removal, and smoothing
  R-peak detection and heart-rate calculation
Not implemented in the supplied code:
  Feature extraction for a classifier beyond RR/heart rate
  CNN architecture or training
  Train/test evaluation of an apnea classifier
  Accuracy, precision, recall, F1, confusion matrix
ECG Signal Processing • 11

## Slide 12
Conclusion
Raw ECG is transformed into a cleaner signal through simple preprocessing.
R-peaks provide heartbeat timing, from which RR intervals and instantaneous heart rate are calculated.
The resulting features form a useful preprocessing foundation for a future sleep-apnea detection model.
Next step: segment ECG/features and train/evaluate a supervised classifier or CNN using the available apnea annotations.
ECG Signal Processing • 12